## Slide 1: code size reduction
Jan 26th 2021

## Slide 2: Antitrust Policy Notice
RISC-V International meetings involve participation by industry competitors, and it is the intention of RISC-V International to conduct all its activities in accordance with applicable antitrust and competition laws. It is therefore extremely important that attendees adhere to meeting agendas, and be aware of, and not participate in, any activities that are prohibited under applicable US state, federal or foreign antitrust and competition laws.
Examples of types of actions that are prohibited at RISC-V International meetings and in connection with RISC-V International activities are described in the RISC-V International Regulations Article 7 available here: https://riscv.org/regulations/
If you have questions about these matters, please contact your company counsel.

## Slide 3: RISC-V International
RISC-V is a free and open ISA enabling a new era of processor innovation through open standard collaboration. Born in academia and research, RISC-V ISA delivers a new level of free, extensible software and hardware freedom on architecture, paving the way for the next 50 years of computing design and innovation.
We are a transparent, collaborative community where all are welcomed, and all members are encouraged to participate. We are a continuous improvement organization. If you see something that can be improved, please tell us. help@riscv.org
We as members, contributors, and leaders pledge to make participation in our community a harassment-free experience for everyone.
https://riscv.org/risc-v-international-community-code-of-conduct/

## Slide 4: Agenda
Table Jump proposal
PUSH + MV proposal
Compiler optimisation and code-speed
Next meeting: 2nd Feb at 7am PDT

## Slide 5: Table Jump
Replace (maybe) 256 JAL destinations with a 16-bit encoding to a jump table
the table entry is MTBLJALVEC + (XLEN/8) * imm_operand
The Jump table contains a pointer to the function, and the LSBs state which link register to use
Two other options are
  emulation mode – put link address and table index into temporary registers, and jump to MTBLJALVEC
  Vector table mode – jump directly to the code, jump to MTBLJALVEC + imm_operand * tablescale
    table scale is 8-bytes to 4096-bytes
https://github.com/riscv/riscv-code-size-reduction/blob/master/ISA%20proposals/Huawei/table%20jump.adoc

## Slide 6: Dynamically linked libraries
Linux uses DLLs, so it needs to dereference the targets of JALs outside the current ELF e.g. a call to GLIBC:
16da: fa6ff0ef jal ra,e80 <symlink@plt>
0000000000000e80 <symlink@plt>:
e80: 00003e17 auipc t3,0x3
e84: 198e3e03 ld t3,408(t3) # 4018 <symlink@GLIBC_2.27>
e88: 000e0367 jalr t1,t3
e8c: 00000013 nop
TBLJAL #n will map to something different in each ELF, so they need to be disambiguated.
- emulation mode should handle this, as the behaviour is software defined.
rv64 has no C.JAL so the benefit of C.TBLJAL will be very high
jump table / vector mode can work if MTBLJALVEC is set correctly for the current DLL

## Slide 7: TBLJAL Benchmark Results
26/01/2021

## Slide 8
MTBLJALVEC.base
TBLJAL #N
continue
Code 0
Code 255
Code N
1<<(scale+2) bytes
Addr 0
Addr N
Addr 255
Addr 1
Xlen
bits
Code 1
Execution
transfers here
Execution
returns here
MTBLJALVEC
points here
Next PC
fetched here
Code 0
Code N
Code 255
ret
ret
MTBLJALCFG.scale==0
Table jump mode
MTBLJALCFG.scale>0
Vector mode
Benchmark results in this presentation

## Slide 9
Get all function calls and count the number each is used
Go through the entries and eliminate all entries that wont gain from substitution (JAL,J) < 3
Change the weight of JALR, and JR entries to be 3*Count
Get the most common (128,256 entries)
Calculate the gains
Static Analysis (Passes through the code, find and count the frequency of each JAL,JALR..).
When selecting the top 128 or 256 entries, we need to give priority to JALR, JR because their replacement save more space, thus their weight is multiplied with 3
Get the top X entries
Calculate the gains, and compensate for the table size
001f8317 auipc t1,0x1f8 e084c2: 18a302e7 jalr t0,394(t1) # 1000648 <__riscv_save_0>
18a302e7 jalr t0,394(t1) # 1000648 <__riscv_save_0>
e084be: xxxx tbljal #x ;#<mapped to __riscv_save_0>
This would saving 6-bytes, but would require a single table entry of 4 bytes, so even a single entry would saves 2 bytes
f61ff0ef : xxxx tbljal
f61ff0ef jal ra,e08432
This would saving 2-bytes, but would require a single table entry of 4 bytes, so we would need at least 3 calls for it to be beneficial

## Slide 10
Chart: Embench Savings
| aha-mont64 | crc32 | cubic | edn | huffbench | matmult-int | minver | nbody | nettle-aes | nettle-sha256 | nsichneu | picojpeg | qrduino | sglib-combined | slre | st | statemate | ud | wikisort
Msaverestore TBLJAL | 0.0038 | 0.0171 | 0.0018 | 0.0045 | 0.0036 | 0.0143 | 0.0044 | 0.0071 | 0.0043 | 0.0018 | 0.0003 | 0.0249 | 0.0033 | 0.0051 | 0.011 | 0.0127 | 0.0015 | 0.0058 | 0.0092
Push pop TBLJAL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0007 | 0 | 0.0199 | 0.001 | 0 | 0.0095 | 0 | 0 | 0 | 0.0044
 | Save Restore | Push Pop
aha-mont64 | 1 | 0
crc32 | 1 | 0
cubic | 1 | 0
edn | 1 | 0
huffbench | 1 | 0
matmult-int | 1 | 0
minver | 1 | 0
nbody | 1 | 0
nettle-aes | 1 | 0
nettle-sha256 | 2 | 1
nsichneu | 1 | 0
picojpeg | 13 | 8
qrduino | 4 | 2
sglib-combined | 2 | 0
slre | 2 | 1
st | 1 | 0
statemate | 1 | 0
ud | 1 | 0
wikisort | 8 | 4
Allocated
Table Size

## Slide 11: Bigger Benchmarks !
Save Restore | 128 Upper Limit |  | 256 Upper Limit |  | No Upper Limit | 
 | Table Size | Saving #1 | Table Size | Saving #1 | Table Size | Saving #1
huawei_iot_application | 128 | 9.43% | 256 | 9.90% | 608 | 10.24%
huawei_iot_protocol | 128 | 6.74% | 256 | 7.37% | 2629 | 9.11%
zephyr_central | 128 | 6.76% | 220 | 7.23% | 142 | 6.83%
zephyr_peripheral | 128 | 6.90% | 142 | 6.83% | 220 | 7.23%
Push Pop | 128 Upper Limit |  |  | 256 Upper Limit |  |  | No Upper Limit |  | 
 | Table Size | Saving #1 | Saving #2 | Table Size | Saving #1 | Saving #2 | Table Size | Saving #1 | Saving #2
huawei_iot_application.elf | 128 | 5.52% | 10.73% | 256 | 5.96% | 11.15% | 604 | 6.28% | 11.45%
huawei_iot_protocol.elf | 128 | 3.66% | 7.64% | 256 | 4.24% | 8.20% | 2632 | 5.98% | 9.87%
zephyr_central.elf | 117 | 3.13% | 8.29% | 117 | 3.13% | 8.29% | 117 | 3.13% | 8.29%
zephyr_peripheral.elf | 128 | 3.77% | 8.28% | 209 | 4.06% | 8.57% | 209 | 4.06% | 8.57%
** Saving #1 measures the incremental saving of adding tbljal to the push/pop compiler output.
** Saving #2 is the cumulative effect of push/pop and tbljal.

## Slide 12: Table Size Vs Saving (IOT_Application)
Chart: 

## Slide 13: Table Size Vs Saving (IOT_Protocol)
Chart: 

## Slide 14: Thank You